## Slide 1: IPv6 Address and Migration Challenges
Peter.J.Willis@bt.com

## Slide 2: Contents - IPv6 Addresses
sTLAs are too small.
NLAs are too small.
IPv6 Address Hierarchies, which one?
Commercial restraints caused by the address allocation rules.
Alternative schemes.
My crystal ball.

## Slide 3: Contents
IPv6 Deployment Challenges
  Cost modelling of migration.
  Suggested strategy for migration
Where are the NGN applications?
Home Networks
  Home gateways
  Addressing & naming in context
  Its about communications not architectures.

## Slide 4: Why is address structure important?
Address structure is more than the total number of bits.
It is the address format & structure that defines the fundamental nature of a network. (Think of the close relationship between IPv4 address structures & the Internet.)
The structure can define the way you build networks. If you get the structure wrong it costs you money to build a network to make that address structure work. (Think of the cost of memory for all those IPv4 routes.)

## Slide 5: IPv6 – Addressing Issues
Registries
eg. 2001::/23
Internet Service
Providers (ISP’s)
Exchanges / Carriers
eg. 2001:618::/35
Sites / SME’s / Home Users
(Site)
eg. 2001:618:100B::/48
Mobile Phones / Home Apps
PDA’s
eg. 2001:618:100B:F8:/64
Internet Assigned
Numbers Authority
Notes: IANA – Internet Assigned Numbers Authority - Top addressing authority – delegates to regional registries:
ARIN – Americas
RIPE – Europe
APNIC – Asia Pacific
Allocation of commercial address space started July 1999 issuing sTLA’s (sub-Top Level Aggregate) – BT allocated 4th sTLA from RIPE [2001:618::/35 ie a prefix written in hex down to the 35th bit in the 128bit address]
Increasingly longer prefixes are handed down the administrative tree down to /48 from which the remaining bits down to /64 are reserved for private network topology assignment within sites

## Slide 6: sTLAs Are Too Small
Currently IPv6 network service providers (NSP) are using sub-TLAs during the boot-strap phase of IPv6.
The sTLA is a /35
The first 13 bits after the /35 is the NLA (Next-Level Aggregation) Identifier.
This NLA space has to be used to address the customers & describe the NSP topology. If the customer is an ISP then they too have to use the NLA space. (Ripe-196)

## Slide 7: NLA Field Explained
Sub-TLA holders have 13bits of Next Level Aggregation (NLA ID)
Example 1
Example 2
NLA1 NLA2
/35 /40 /48
NLA1 NLA2
/35 /43 /48
NLA1, 5 bit = 32 ISPs & NLA2, 8 bits = 256 End sites
NLA1, 8 bits = 256 ISPs & NLA2, 5 bits = 32 End sites
Notes: Section 4.2.8.Allocations to NLA Registries of RIPE-196 “Provisional IPv6 Assignment and Allocation Policy Document” specifies that “TLA Registries with ISP customers may use their 13 bits of BLA address space to create an addressing hierarchy for those ISPs” So for example a TLA Registry may create an hierarchy as in example 1. So example 1 means that a TLA Registry can allocate 8 bits off address space to 32 ISPs. This causes two problems:
The receiving ISP can only allocate 256 /48’s to customers.
If the TLA Registry has allocated itself a NLA allocation, then according to RIPE-196 “A TLA Registry receiving a request for a subsequent NLA allocation must submit the request to the relevant Regional IR for a second opinion”

## Slide 8: Sub-TLA IDs - Use the reserved field
NLA field can grow from 13 bits to 19 bits using the reserved bits
subTLA NLA SLA Interface
2001:618::/29 19 16 64 bits
/29 /48 /64
19 bits = 524,288 /48’s per subTLA
/29 /35 /48 /64
subTLA NLA SLA Interface
2001:618::/35 13 16 64 bits
13 bits = 8,192 /48’s per subTLA
RES

## Slide 9: Using the NLA Hierarchically
In NGNs with billions of attached devices the only way networks will scale will be with a deep hierarchy.
To keep the routing table to a minimum size each layer of the hierarchy must do near perfect routing aggregation.
Lets explore some network hierarchies and see how many bits are required:

## Slide 10: Network Addressing Scheme1
Hierarchical
Level
Size
Number of bits
Continent
7
3
Country
221
8
State/County
64
6
Town
128
7
Line/Site
1024
10
Total = 34 bits
Remember current NLA size = 24 bits. +8 more reserved bits

## Slide 11: Network Addressing Scheme2
Hierarchical
Level
Size
Number of bits
International backbone
10 PoPs
4
Continental backbone
20 PoPs
5
Country backbone
1000 PoPs
10
Lines to customers
1024 lines
10
Total = 29 bits
Remember current NLA size = 24 bits. +8 more reserved bits

## Slide 12: Network Addressing Scheme3 and NLA Size Conclusion
Assume very efficient address allocation without any network hierarchy (not a recommended design!)then how many lines to customers could we have with a 24 bit NLA? 2^24 = 16 Million.
Using the Huitema-Durand method then 31 bits is required to address 30 Million homes. (See notes)
Simply a NLA of 24 bits is not big enough for a global network operator nor big enough for a UK operator aiming to reach every home.
A 34 bit NLA should be sufficient.
Notes: draft-durand-huitema-h-density-ratio-01.txt describes a good ratio for representing address utilisation taking account of network hierarchies. The proposed HD value is:
log(number of allocated objects)/log(maximum number of allocatable objects)
expressed as a percentage. By inspection of existing networks they suggest a comfortable HD ratio is 80%.
This implies the number of bits required to address O objects is given by
(Log O)/0.24 (Using Log 10)
This can be mathematically explained with the following. Take a population of subnets, each subnet contains a random number of hosts, assign to the subnet the lowest power of 2 larger than or equal to the number of hosts. Over a large population the ratio of the sum of the power of 2s divided by the sum of the number of hosts is 75%. A power of 2 has to be used to give perfect address aggregation, that is only 1 route per subnet.
For every level of network hierarchy the maximum utilisation is 75%. For example for 3 levels of network hierarchy (local, national, international) would yield an efficiency of 0.75^3 == 42%.
The number of layers of hierarchy required is given by Log O/Log R. Where O = number of objects. And R = maximum number of objects that can be aggregated into 1 node at the next highest level of the network hierarchy.
Hence we can say that the maximum utilisation is = 0.75^(Log O/Log R)
This implies the number of bits required to address O objects is given by
3.32Log(O/0.75^(Log O/Log R))
So to address 1000000 objects the HD formula suggests 25 bits. The theoretical maximum formula suggests 21bits. The HD ratio although subjectively defined therefore appears reasonable.
Applying the HD formula to the UK for a UK operator wishing to address the population of 30 Million homes, if each home is a site would require 31 bits. Applying the HD formula to a European operator wishing to address JUST every enterprise of which there is 18.4 Million in Europe would require 30 bits.

## Slide 13: IPv6 Address Hierarchies, which one?
FP
RES
TLA NLA SLA INTERFACE
ID ID ID ID
/3 /16 /24 /48 /64
RFC 2374 “An Aggregatable Global Unicast Address Format”
TLA sub NLA SLA INTERFACE
ID TLA ID ID ID
FP
RES
/3 /16 /29 /35 /48 /64
RIPE 196 “Provisional IPv6 Assignment and Allocation Policy Document”
TLA sub NLA SLA INTERFACE
ID TLA ID ID ID
FP
/3 /16 /29 /48 /64
RFC 2450 “Proposed TLA and NLA Assignment Rules
Notes: Initial IPv6 Sub-TLA ID Assignments
Technical input to IANA in the fall of 1998. IANA have the responsibility for the management of the IPv6 address space.
RFC 2450 specifies that TLA assignments will be done in two stages. First stage is to allocate a Sub-TLA ID. All Sub-TLA ID are assigned from one TLA ID.
IANA have allocated blocks of 64 /29’s to IANA, APNIC, ARIN & RIPE NCC. 124 blocks of 64 /29’s are marked for future assignment. 8,192 /29 Sub-TLA ID are available in total, which equals the number of possible TLA ID. When the Sub-TLA holder has assigned more than 90% of the NLA ID for their Sub-TLA ID they will be allocated a TLA ID. The Sub-TLA ID does not have to be returned.
However the Registries have implemented a “slow-start” procedure for their blocks of /29’s, initially allocating /35 Sub-TLA ID to organisations.
Slow-start = 8,192 /48s
RFC2450 = 524,288 /48s
RFC 2374 = 16,777,216 /48s

## Slide 14
IPv6 Address Hierarchies,even more?
global routing Subnet INTERFACE
prefix ID ID
n bits m bits 128-n-m bits
draft-ietf-ipngwg-addr-arch-v3-06.txt Now an RFC.
See also
http://www.apnic.net/meetings/12/sigs/joint_ipv6.html
RIPE 40 1st October Prague
http://www.ripe.net
/ripe/meetings/current/ripe-40/index.html

## Slide 15: Commercial restraints caused by the address allocation rules.
The TLA/NLA/SLA structuring and address assignment rules drives a commercial model of customers dependent on Tier 2 ISPs dependent on Tier 1 ISPs.
This is not the way it works with 3G!
Slow start rules provide unfair competitive advantage to established & large networks.
Address utilisation targets if set too high cause a flattening of network hierarchy which leads to higher engineering costs.
Notes: The more bits we can give to the network hierarchy the simpler routing becomes. Given sufficient bits then routing becomes trivial. Reducing the number of bits in the address available for hierarchy will increase the number of routing entries in the routing table, this means more memory and CPU is required in the routers.

## Slide 16: Alternatives
draft-hain-ipv6-pi-addr-00.txt “An IPv6 Provider-Independent Global Unicast Address Format”. The users IPv6 address is derived from their latitude and longitude.
Increase the number of bits in the global routing prefix by reducing the number in the interface id. Then allow any ISP unqualified address space.
The ideal situation is that every ISP has enough address space to address everyone.

## Slide 17: My Crystal Ball
In the short term looking to see some improvement in the IPv6 address structure and allocation rules in the current RIRs considerations.
In the long term I expect IPv6.1 which will make much better use of the 128 bit address space.

## Slide 18: IPv6 Deployment Strategy: Cost Modelling of IPv6 Migration
Understanding the business case for deploying IPv6 is the first key step.
Understanding the costs of IPv6 is key and it is the costs that will form a significant obstacle.
Your IPv6 deployment strategy should seek to minimise costs and maximise commercial advantages.

## Slide 19: IPv6 Migration Costs Study
The study looked at the whole costs of migrating to IPv6 for the following scenarios:
  A Big or Tier1 ISP
  A Big enterprise
  A SME
  A Dial-ISP
The study examined the costs of migrating now and migrating in 5 years time.
Extra maintenance costs included.

## Slide 20: IPv6 Migration Costs Assumptions
Attempted to include all costs, including new software, memory, hardware, OSS and desktop upgrades.
Extra maintenance costs assume the extra costs of running IPv6 on an existing IPv4 network. That is assuming a dual-stack scenario.
Once IPv4 is phased out then extra-maintenance costs no longer apply.
Application migration costs not included but allowed for with BITS s/w for legacy IPv4 applications that could not be migrated.

## Slide 21: Big ISP Migration Costs Big ISP equivalent to a Tier 1 ISP
Now
+5 Years
Cost/
customer
£1K
£2K
£4K
Max cost
Min cost

## Slide 22: Big ISP Extra Maintenance Costs Big ISP equivalent to a Tier 1 ISP
Now
+5 Years
Cost/
customer
£50
£100
£200
Max cost
Min cost

## Slide 23: Big Enterprise Migration Costs 100,000 Desktops
Now
+5 Years
£1K
Max cost
Min cost
£500
£250
Cost/
Employee

## Slide 24: Big Enterprise Extra Maintenance Costs 100,000 Desktops
Now
+5 Years
£100
Max cost
Min cost
£50
£25
Cost/
Employee

## Slide 25: SME Migration Costs
Now
+5 Years
£1K
Max cost
Min cost
£500
£250
Cost/
Employee

## Slide 26: SME Extra Maintenance Costs
Now
+5 Years
£10
£5
Cost/
Employee
£15

## Slide 27: Dial-ISP Migration Costs 1 Million lines
Now
+5 Years
Max cost
Min cost
£20
£10
Cost/
Line
£30

## Slide 28: Dial-ISP Extra Maintenance Costs 1 Million lines
Now
+5 Years
£5
£2.5
Cost/
Line
£7.5

## Slide 29: Recommendations
Do not upgrade to IPv6 now but plan to do it in about 5 years time.
Ensure as kit & software is churned or upgraded for operational reasons that it is upgraded to be IPv6 capable.
Start work on your IPv6 upgrade strategy now.
Waiting for the killer IPv6 application or until your competition has upgraded to IPv6 could be more expensive than a planned gradual upgrade in IPv6 capability.
Once IPv6 is deployed shortening the life time of IPv4 will reduce maintenance costs.

## Slide 30: Where are the NGN applications?
NGN is not the same as IPv6.
What is stopping NGN applications being deployed in IPv4?
If you have an application but can’t deploy it because of a lack of IPv4 addresses or because IPv6 not widely deployed we need to know!
Notes: http://www.groupbt.com/mediacentre/position/broadband.htm
http://www.groupbt.com/mediacentre/position/llu.htm

## Slide 31: Home Networks and IPv6
When thinking about naming & addressing we need to consider the context of the communications.
The residential/home gateway may be a better place to manage communications in & out of the house.
The Internet’s end-to-end architecture may no longer be appropriate. Architectures develop as technology changes.
“Meta networks” with “intelligent” translation of messages at the edge of network domains may now be more appropriate. SIP & NAT are examples. This gives security & control (no more dDOS attacks).
Given a “SIP” that works then global IP addresses are no longer needed - communications routed on names. (XML routing is another alternative tech.)

## Slide 32: Conclusion
As an industry we need to make sure we don’t make the same “Class A,B,C” mistake we made with IPv4. That is not thinking about the future.
If IPv6 happens the costs of migrating to it can be mitigated by an IPv6 upgrade strategy applied now.
Don’t become religious about architectural principles that were created in a different technological era.

## Slide 33: Thank you.
Peter.J.Willis@bt.com